## Slide 1: FARM TOOLS & EQUIPMENT
Farm tools and equipment are devices or implements used to carry out certain activities on the farm.

## Slide 2: CATEGORIES OF FARM TOOLS AND EQUIPMENT
They are categorized into five major groups namely:
Garden tools and equipment
Workshop tools and equipment
Livestock production tools & equipment
Plumbing tools and equipment
Masonry tools and equipment

## Slide 3: Reasons for using farm tools and equipment
To increase efficiency on the farm
To enhance production
To enhance safety on the farm

## Slide 4: Precautions observed when using farm tools and equipment
Handle tools carefully and correctly
Use a tool for the job it was designed for
Maintain the tool in good working condition
Learn how to use a tool or operate a piece of equipment before use
Dress appropriately when using farm tools and equipment
The work should be firmly secured where possible
Store farm tools in safe place such as in tool racks
Avoid wearing loose clothes especially when operating workshop tools and equipment
Avoid working on dangerous grounds such as on slippery floors

## Slide 5: A. CROP PRODUCTION TOOLS & EQUIP
Removing roots, & stones
Breaking heavy soils
Digging hard rocks
Maintenance of Fork Jembe
Clean after use
Replace handle if broken
Paint blade to avoid rusting
1. FORK JEMBE
USES OF FORK JEMBE

## Slide 6: 2. SICKLE
USES OF SICKLE
Cutting back pyrethrum stalks
Harvesting rice & Grasses
Maintenance of sickles
Replace broken handle
Clean after use
Sharpen blade regularly
Paint blade to avoid rusting

## Slide 7: 3. PICK AXE
USES OF PICK AXE
Removing roots & stones
Breaking heavy soils
Digging hard soils
Maintenance of Pick axe
Replace handle if broken
Paint blade to avoid rusting
Clean after use
Sharpen blade regularly

## Slide 8: 4.MANURE FORK
USES OF MANURE FORK
Digging and collecting manure & trash
Maintenance of manure fork
Paint blade to avoid rusting
Replace blade if broken
Clean after use

## Slide 9: 5. PRUNING SAW
USES OF PRUNING SAW
Pruning hard branches of coffee, citrus etc
Maintenance of pruning saw
Clean after use
Replace handle if broken
Paint blade with oil
Sharpen blade regularly

## Slide 10: 6. RAKE
USES OF RAKE
Used in nursery preparation
Removes trash from seedbed
Levels the ground
Maintenance of Rake
Paint to prevent rusting
Replace broken handle
Clean after use

## Slide 11: 7.PRUNING SHEARS
Uses of pruning shears
Used for trimming hedges & shrubs
Maintenance of pruning Shears
replace handle if broken
clean after use
paint to prevent rusting

## Slide 12: 8. SECATUERS
USES OF SECATUERS
Pruning soft branches
Maintenance of secateurs
Oil moving parts
Sharpen regularly
Clean after use
Paint to avoid rusting

## Slide 13: 9. TAPE MEASURE
USES OF TAPE MEASURE
Used for measuring distances
Maintenance of T. measure
Clean after use

## Slide 14: 10. SPRINKLER
USES OF SPRINKLER
Used for irrigating crops
Maintenance of sprinkler
Unblock the nozzles
Clean after use
SPRING LOADED SPRINKLER

## Slide 15: 11. KNAPSACK SPRAYER
Used for spraying chemical solutions
Maintenance of Knapsack
clean well after use
Unblock the nozzles
Spray tank
Trigger
Hose pipe
Pneumatic lever
Strap
Hand lance
Nozzle

## Slide 16: 12. GARDEN FORK
USES
Weeding nursery
Lifting seedlings
Collecting Manure
MAINTAINANCE
Clean after use
Paint metallic part

## Slide 17: 13.GARDEN TROWEL
USES
Lifting seedlings
Loosening soil in the nursery
MAINTAINANCE
Clean after use
Replace handle if broken
Paint mettalic part

## Slide 18: 14.HOSE PIPE
USES
Used to convey water from a tap to where its needed
MAINTENANCE
Repair any leakages
Clean after use
Don’t keep pipe I the sun

## Slide 19: 15. AXE
USES
Felling big trees
Cutting tree stumps
Splitting firewood
MAINTENANCE
Sharpen cutting edge regularly
Replace broken handle
Oil the cutting edge

## Slide 20: 16. PANGA
USES
Cutting bushes, shrubs & grass
Clearing land
Harvesting crops
MAINTENANCE
Oil for long storage
Repair broken handle
Sharpen cutting edge

## Slide 21: 17. JEMBE
USES
Cultivation
Planting
Weeding
Harvesting root crops
MAINTAINANCE
Clean after use
Sharpen the blade
Replace handle if broken
Keep the blade dry

## Slide 22: 18. FORK JEMBE
USES
Cultivating areas with rhizomatous roots
Cultivating stony ground
Harvesting root crops
Digging sticky ground
MAINTAINANCE
Clean after use
Replace broken handle
Paint the pongs

## Slide 23: 19. SHOVEL
USES
Moving soil (earth) or manure
Scoop mortar & concrete
MAINTENANCE
Keep handle firmly fixed
Clean after use
Replace handle if broken
Oil for prolonged storage

## Slide 24: 20. SOIL AUGER
USES
Digging holes for fixing fencing posts
Scooping soil samples for testing
MAINTAINANCE
Clean & dry after use
Lubricate moving part
Oil for storage to prevent rusting

## Slide 25: 21. WATERING CAN
USES
Used for overhead irrigation
MAINTAINANCE
Keep the holes of the rose clean
Fix leaking/broken part
Paint to prevent rusting
Keep empty & dry

## Slide 26: 22. KNAPSACK SPRAYER
USES
Spraying chemicals to crops
Spraying livestock to control parasites
MAINTAINANCE
Wash after use
Replace worn out parts
Unblock nozzles
Grease moving parts

## Slide 27: B. LIVESTOCK PRODUCTION TOOLS & EQUIPMENT
Holding milk in transit
Maintenance of milk churn
Thorough cleaning
Sterilization after use
How to sterilize the equipment
Wash in hot water
Wash with disinfectant
Dry in hot sun
1. MILK CHURN/CAN
USE OF MILK CHURN/CAN

## Slide 28: 2. BULL RING & LEAD STICK
USES
Restraining livestock
MAINTAINANCE
Replace the ring if broken
Use a strong stick
Keep the stick dry

## Slide 29: 3. HALTER
USES
A special rope designed to restrain & lead animals
MAINTAINANCE
Always keep dry

## Slide 30: 4. BOLUS GUN
USES
Shooting solid drugs or tablets into the throat of an animal
MAINTAINANCE
Clean & disinfect after use
Store in a dry place

## Slide 31: 5. DRENCHING GUN
USES
Giving liquid drugs into the mouth of an animal
MAINTAINANCE
Wash & disinfect after use
Repair broken parts
Tighten
Unblock nozzle if broken

## Slide 32: 6. BURDIZZO
USES
Bloodless castration of male livestock
Docking in sheep
MAINTAINANCE
Oil the pivot
Replace handle if broken
Tighten loose parts

## Slide 33: 7. ELASTRATTOR
USES
Expanding the rubber ring when fixing it for castrating, docking, or dehorning animals
MAINTAINANCE
Oil the pivot
Tighten loose parts
Repair broken handle

## Slide 34: 8. EAR NOTCHER
USES
Notching the ear for identification purposes
MAINTAINANCE
Clean & disinfect after use
Oil or grease moving parts
Repair broken parts
Tighten loose parts

## Slide 35: 9. HOOF CUTTER
USES
Trimming/cutting overgrown hooves of livestock
MAINTAINANCE
Oil the pivot
Sharpen the cutting edge
Keep dry to prevent rusting

## Slide 36: 10. TEETH CLIPER
USE
Cutting milk teeth of piglets
MAINTAINANCE
Tighten loose nuts
Oil/grease moving parts
Clean & disinfect after use

## Slide 37: 11. TROCA & CANULA
USE
Piercing the left side of rumen to release accumulated gases
MAINTAINANCE
Clean & sterilize after use
Store in safe place

## Slide 38: 12. WOOL SHEARS
USE
Shearing, cutting or clipping wool in sheep
MAINTAINANCE
Sharpen the cutting edge
Oil for prolonged storage
Store in a dry place

## Slide 39: USE
Spraying livestock with chemicals to control external parasites
MAINTAINANCE
Wash after use
Oil shaft & valve
Replace worn out nozzles & seals
Unblock nozzles

## Slide 40: 14. STRIP CUP
USE OF STRIP CUP
Checking whether a cow has mastitis
Yellow clots will be seen in the black plate if cow has mastitis
Maintenance of strip cup
Clean well after use
Keep it dry
Store in clean dry place

## Slide 41: 15. MILK STRAINER
USE
Sieve milk to remove hair & dirt
MAINTAINANCE
Clean after use then
sterilize
Replace filter pads
Keep perforated disks free of dirt

## Slide 42: C. WORKSHOP TOOLS & EQUIPMENT
Fine sawing
Small work cutting
Maintenance of back saw
Teeth setting
Tighten loose screws & nuts
Straighten the blade if bent
Repair broken handle
Sharpen regularly
Cleaning after use
BACK SAW
Has rigid frame on the back
USE OF BACK SAW/TENON

## Slide 43: 2. BRACE
USE
Drilling/Boring holes in wood using bits
MAINTAINANCE
Grease the revolving part
Store bit in a casing after use
Replace lost bolts & nuts
Tighten any loose parts

## Slide 44: 3. HAND DRILL
USE
Boring holes in metal using bits
MAINTAINANCE
Replace worn out parts
Oil & grease moving parts
Oil bits for prolonged storage
Tighten loose parts
Clean after use

## Slide 45: 4. WOOD CHISEL
USE
Making cavities in wood
Trimming off rough edges in wood
MAINTAINANCE
Sharpen the cutting edge
Keep it in a tool rack or box for proper storage
Hammer using wooden or plastic mallet only
Replace broken/worn out handles
Grind the level & edge to maintain the angle
Clean after use

## Slide 46: 5. COLD CHISEL
USE
Cutting metal rods & plates
Cutting heavy gauge metal sheet
MAINTAINANCE
Sharpen the cutting edge
Remove the mushroom head after a period of use
Oil for prolonged storage to avoid rusting

## Slide 47: 6. CLAW HAMMER
USE
Driving in or removing nails from wood
Straightening crooked nails
MAINTAINANCE
Keep handle firmly fixed
Replace broken handles
Store properly in a tool box
Oil the head for prolonged storage to avoid rusting

## Slide 48: 7. SLEDGE HAMMER
USE of sledge hammer
Demolishing farm structure
Crushing or breaking big stones in masonry work
Driving in wedges when splitting wood
MAINTAINANCE
Keep handle firmly fixed
Replace broken handle
Oil the head for prolonged storage

## Slide 49: 8. MALLET
USE
Hitting /drive wood chisels & wooden pegs
Hitting frames when fitting them together
MAINTAINANCE
Replace broken parts
Do not use to drive in nails
Store in a dry place after use

## Slide 50: 9. MARKING GAUGE
USE
Marking a line which is parallel to the edge of a piece of wood
MAITAINANCE
Replace broken parts
Replace the screw if lost
Sharpen the pin if blunt

## Slide 51: 10.SPOKE SHAVE
USE
Smoothening curved wooden surfaces or edges
MAINTAINANCE
Sharpen the blade regularly
Repair & replace broken or worn out parts
Clean after use
Tighten loose bolts & nuts
Replace lost bolts & nuts

## Slide 52: 11.RIVETING MACHINE
USE
Fixing rivets when joining two pieces of metal
MAINTAINANCE
Grease or oil the moving parts
Keep safe after use
Cleaning after use

## Slide 53: 12. BOW SAW
USE
Cutting wood where curved pattern is required
Pruning tree crops
MAINTAINANCE
Set & sharpen the teeth regularly
Tightly fix blade on the frame
Oil the blade for prolonged storage

## Slide 54: 12. COMPASS SAW/KEY HOLE SAW
USE
Used to make curved or irregular slits on thin wood & boards
Cutting holes especially key holes
MAINTAINANCE
Set & sharpen the teeth regularly
Tighten loose nuts & screws
Oil the blade for prolonged storage

## Slide 55: 13. KEY HOLE/PAD SAW
USE
Cutting small holes and slots in wood
It’s a smaller version of the compass saw
MAINTAINANCE
Set & sharpen the teeth regularly
Tighten loose nuts & screws
Oil the blade for long storage

## Slide 56: 14. CROSS-CUT SAW
USE
Cutting wood across the grain
MAINTAINANCE
Set & sharpen the teeth regularly
Oil the blade for prolonged storage

## Slide 57: 16. RIP SAW
USE
Cut wood along the grain
The teeth are perpendicular to the blade
Filed at right angle to the blade
MAINTAINANCE
Set & sharpen the teeth regularly
Tighten loose nuts & screws
Oil the blade for prolonged storage

## Slide 58: 17. TENON/BACK SAW
USE
Joining work to cut tenon joints in wood
Fine- sawing of small pieces of timber
MAINTAINANCE
Set & sharpen the teeth regularly
Tighten loose nuts & screws
Oil the blade for prolonged storage

## Slide 59: 18. HACK SAW
USE
Cutting metal rods & pipes
Dehorning mature cattle
MAINTAINANCE
Ensure the blade is tightly fixed to the frame
Replace or repair broken parts
Replace worn-out blades
Oil for prolonged storage

## Slide 60: 19. JACK PLANE
USE
Smoothening & cleaning up surface of wood to obtain a fine, even surface
MAINTAINANCE
Sharpen the blade if blunt
Replace or repair broken parts
Replace lost bolts and nuts
Tighten any loose nuts and bolts
Clean and oil after use

## Slide 61: 20. WOOD CHISEL
USES OF WOOD CHISEL
Cutting grooves on wood
Chopping off rough wood surfaces
Maintenance of wood chisel
Use with a mallet
Replace broken handle
Grind the bevel to maintain the angle
Sharpen if necessary

## Slide 62: 21. SCREW DRIVERS
USE
Driving in or out screws
MAINTANANCE
Flatten dented tips
Use the right size of the screwdriver for a given job
Put screwdrivers in a tool rack or box for safe storage

## Slide 63: 22. SPANNERS
USE
Tightening & loosening nuts and bolts
MAINTAINANCE
Oil to prevent rusting
Clean after use
Oil moving parts, in case of adjustable spanner

## Slide 64: 23. SPIRIT LEVEL
USE
Align surfaces vertically or horizontally
MAITAINANCE
Keep safely in its case after use

## Slide 65: 24. TINSNIP
USE
Cutting thin sheets of metal
MAINTAINANCE
Sharpen the cutting edges if blunt
Oil the pivot to reduce friction
Keep it in a safe place after use to avoid injuries
Store in a dry place to avoid rusting

## Slide 66: 25. TRY SQUARE
USE
Making marks or laying out objects at right angle
Measuring lengths
Checking evenness of surface
MAINTAINANCE
Avoid rubbing against objects
Store safely after use

## Slide 67: 26. G- CLUMP
USE
Holding objects firmly and squarely on the bench during various operations
MAITAINANCE
Grease the threads
Clean after use
Store safely in a dry place

## Slide 68: 27. SASH CLAMP OR T- CLAMP
USE
Holding structure like windows & tables when working on them
MAINTAINANCE
Grease the threads
Clean and dry after use
Store properly in a dry place

## Slide 69: 28. ANVIL
USE
Used as a surface on which to shape hot pieces of metal using a hammer
MAITAINANCE
Clean after use
Oil to avoid rusting
Remove any metal pieces from its surface after every use

## Slide 70: 29. WIRE/MONKEY STRAINER
USE
used for tightening barbed wires when fencing
MAITAINANCE
Oil and grease the chains
Repair or replace broken parts

## Slide 71: 30. CRAW BAR
USE
Removing nails and staples from wood
MAINTAINANCE
Store in a safe place to avoid injury

## Slide 72: 2. HAND SAW
Used for cutting wood.
Types of Hand saw
Rip saw
Cross-cut saw
Teeth
Heel
Toe
Blade
Back
Handle

## Slide 73: PARTS OF WOOD CHISEL
Handle
Head
Shoulder
Bevel edge blade
Cutting edge

## Slide 74: JACK PLAIN
Plain bottom
Heel
Adjusting knob
Handle
Lever cap
knob

## Slide 75: D. MASONRY TOOLS & EQUIPMENT
Laying and firming mortar between joints of bricks or building stones
Applying mortar when plastering
MAINTAINANCE
Keep in a safe place
Clean and dry after use
USE
1. MASON’S TROWEL

## Slide 76: 2. BOLSTER/MASON’S CHISEL
USE
Used for dressing building stones
MAINTAINANCE
Sharpen the cutting edge regularly
Remove the mushroom head after a period of use

## Slide 77: 3. PLUMB- LINE
USE
Aligning objects such as bricks, and building stones and upright surfaces vertically
MAINTAINANCE
Replace the string if worn out
Clean and store properly after use

## Slide 78: 4. METAL FLOAT
USE
Used for smooth finishing of masonry work by spreading cement paste over plastered floors and walls
MAINTAINANCE
Clean and store properly after use

## Slide 79: 5. WOOD FLOAT
USE
Holding small amount of mortar
Used together with the trowel to seal joints between bricks
MAINTAINANCE
Fix the handle firmly
Repair broken parts
Clean after use
Store properly

## Slide 80: E. PLUMBING TOOLS & EQUIPMENT
Holding, tightening and loosening metal pipes and fittings
MAINTAINANCE
Lubricating the adjusting screws
Oil to prevent rusting
Clean and store properly after use
use
1. PIPE WRENCH/STILLSON WRENCH

## Slide 81: 2. PIPE CUTTER
USE
Cutting plastic and metal pipes
Suitable for cutting pipes with an internal diameter of up to 100mm
MAINTAINANCE
Clean well after use
Grease or oil the moving parts

## Slide 82: General maintenance practices carried out on farm tools & equipment
Use the right tool for the right job
Always follow the manufactures instructions when using any tool
Clean and dry tools and equipment after use
Sharpen cutting edges regularly
Replace broken and worn out parts
Store tools in safe places such as in toolboxes or tool racks
Oil metallic parts in case of prolonged storage to avoid rusting
Lubricate moving parts
Avoid rubbing tools against each other

## Slide 83: Reasons for maintaining farm tools and equipment
To avoid injury to the user
To increase durability
To increase efficiency
To avoid cost of repair and replacement